# Threading the Machine

Objective:  The students will be able to thread the machine, wind the bobbin, and correctly place the bobbin in the case.

Supplies:  	Thread

Bobbin

Sewing machine

- Winding the Bobbin.

Have each student pick a spool of thread and a bobbin and wait at his/her machine for instructions.

- Disengage the hand wheel.

- Put thread on the spool pin, and the bobbin on the bobbin winder.

- Follow the arrows on the machine to thread the bobbin.

- Lock the bobbin into place on the bobbin winder.

- Wind the bobbin.

- Re-engage the hand wheel.

- Unlock the bobbin.

- Threading the Machine.

Demonstrate how to thread the machine.  Tip: When threading the needle, lick fingers and run over the eye of the needle and the end of the thread.  Tip:  Thread the needle from the front to the back.

Students need to practice this 5 times.  The teacher will check them off.

- Changing the Needle.

Show students how to change the needle if it becomes bent, broken or dull.

- Lower the presser foot.

- Unscrew the needle from the needle shaft.  Hold onto the needle as you do this.

- Remove the old needle and throw it away.

- Replace with a new needle.  The flat side of the needle always goes towards the back of the machine.

- Make sure the needle is all the way in; tighten the screw down.

- The bobbin and bobbin case.

- Put the bobbin in the bobbin case clockwise.  When you pull on the thread, the bobbin will turn clockwise.

- Thread it through the bobbin case.  The teacher needs to check everyone off at this point.

- Put the bobbin case into the machine; you will hear it click into place.  The teacher needs to check everyone off at this point.

- Demonstrate how to pull bobbin thread up.

Students need to repeat this procedure 5 times.

- Summary.

Threading the machine is one the most crucial parts of sewing.  Most sewing machine problems are a result of incorrect threading.  If the machine is not threaded correctly, the sewing machine will not sew.

Points to Discuss:

- How many threads do you need in order to sew on a sewing machine?

- What way do you put the bobbin into the bobbin case?

- List the four steps that have to be done before winding a bobbin.

- Where does the bobbin case go at the end of the day?